Network checklist for EBL/WBF championships
New version
This version was converted from Word to Opendoc, and adapted to new insights and hardware. Comments are highly appreciated.
## Preparation
At a venue we can setup a network in various ways. How we do it depends on the venue, and what they can do, or allow us to do.
There are basically three ways. We describe them here, and document what we need from the venue, and what we need to do ourselves.
## The layer 1 approach
This is the simplest way for the venue, and also the best way to ensure everything works, assuming we do not make any mistakes ourselves. With this approach we only use the wiring of the building, and provide all the equipment ourselves. This is basically the way we did Dublin 2012, Tromsø 2015 and Istanbul 2019.
From the building we need to know exactly which network ports in the various rooms are connected to which patching location. These locations go with various names. MER/SER, for Main Equipment Room/Secondary Equipment Room is used, sometimes they are called comms-rooms, sometimes just patch panels. They are the rooms/closets where the other end of the cable of all the network ports end up. They tend to be in the dirtiest part of the building...
If there is more than one of these locations, they should be interconnected in some way, usually nowadays with fiber. We then need to know the topology, which free fibers go from where to where. Also we need to know about fiber patch cables. Do they have cables that connect to our SFP modules? We for now only have multi-mode fiber SFP’s, but SFP’s can be borrowed and are cheap to buy nowadays. UTP copper connections are also possible, those are easier to handle.
The next thing is physical access to these rooms. Are we allowed to get in, how often, how quick, which procedure? Are we allowed installing equipment in these rooms, is there power, rack space?
If all this can be handled we will install the firewall (Netgate) in one of the rooms, connected to a switch of ours and install switches in every other location if necessary.
Questions to be answered by venue:
1. Can we get access, supervised if necessary, to all the locations with patch panels that connect all the network ports in all rooms we need to use?
2. Are we allowed to install some equipment at these locations? A maximum of 2 devices, each 1RU high will be needed. They should be able to get some power. They need not be in a rack, on a table or on top of a cabinet is fine for us.
3. Are the locations interconnected with unused cabling that we can use? If this interconnection is fiber we need specifications for the type of connectors used, and the patch cables available. We use SFP modules in our equipment.
## The layer 2 approach
This is a sort of middle ground. In this approach the venue provides for the VLAN’s we need and is responsible for connecting all the various network ports to the VLAN we specify. How they transport these VLAN’s is up to them.
We need to know which VLAN numbers they can give to us, and adjust our equipment to that. In Veldhoven 2011, where we first used this approach, we were assigned VLAN 30-35, but this is surely not a standard. In Budapest 2016 we used the same, and Wroclaw 2016 should be the same. In Orlando it was 161-170. By now we are going to use more VLAN’s, so the safest thing is to ask for VLAN 30-39. Any other range of 10 VLAN’s will be fine, but we prefer the first one to be a multiple of 10, although this is not strictly necessary. We will call the first VLAN number BASE.
 Discuss in painful detail with the building’s network managers about trunking. For all trunks we use the standard that all are transported, with BASE untagged and the rest tagged. Untagged is also called native. The experience in Oostende was pretty bad, and should have been communicated much better. Running the network ourselves is preferred, if it is possible.
The reason why we use BASE untagged, is that it is the MGMT network, and the IP addresses of the switches for management purposed are on the MGMT network. This means when VLAN numbers vary per tournament it is good to be able to plug a laptop in a trunk port and manage the switch.
In this approach we need to know nothing about the topology, since the venue is taking care of that.
We do need to have a procedure to connect ports to a VLAN, and we need to make agreements about communication to their staff and speed of handling.
We must have a place to connect our firewall(Netgate) to their infrastructure and the Internet. This will probably be in one of their MER/SER locations. It can be on another location, but in a locked location somewhere is safer.
They must be able to configure the trunk ports in the way we like them, or we need to pre-test.
1. Can you supply us with at least 3, but preferably 10 VLANs? We preferably use numbers 30-39, but any other range is ok, recently we used 160-169, say BASE to BASE+9.
2. Can you connect at our request any network port with one of these VLANs, specified by us?
3. Can you connect at our request any network port with an 802.1q trunk, containing some tagged VLAN’s and one untagged VLAN, specified by us? Normally we use all our VLAN’s, BASE untagged, rest tagged.
4. Do you have some, or all, ports with POE? This is relevant for cameras or WiFi access points.
5. Can we install our firewall somewhere in your network to connect to your switches and Internet? We use one 802.1q trunk for this. Same as above.
In these sort of places the site usually also has some wireless infrastructure, sometimes with multiple SSID support. Questions:
1. Can you give us some SSID’s on your wireless?
2. A public player network, preferably without password, connected to Internet
3. Some(2,3) SSID’s connected to some of our VLAN’s, with passwords chosen by us.
Any port blocking?
Is https://zeus.hrwebservices.net:2096/ reachable?
Does the BBO app work?
Is the external IP address reachable from building WiFi?
Sometimes these places have video distribution networks. What can they do?
## The layer 3 approach

This is deprecated. Use layer 1 or layer 2, because layer 3 will be a pain in the ...
This is the approach where the venue does everything, and we just connect our equipment. We do not use the firewall or core switch. This was the approach in Poznan 2011.
The venue must be able to provide us with at least 3 and preferably 5 VLANs, and just as in the layer 2 approach they must set up the connections to the various network ports.
But in this case they also must set up all the policies we have. Some non-complete examples:
- HTTP to an external address should go to a particular server of ours
- Some hosts (BBO) on the WBF VLAN should be able to go to the scoring server, but others should not.
- A particular host on the DMZ VLAN should be allowed to contact the scoring server, but others should not
Again we would need to make agreements on communication and speed of handling.
1. Can you supply at least 3, but preferably 5 logical networks?
2. Can we specify the IP addresses, and DHCP ranges?
3. Can we supply you with the access rules, down to the TCP or UDP port level?
4. Can you connect at our request any network port with one of these networks, specified by us?
## Common
In all case we would need to know in advance the nature of the Internet connection(s) we would be provided with. These are:
- Speed. Our heaviest use is video for BBO, about 3 Mbps per stream. With 12 BBO booths 50 Mbps up/down is just sufficient, a bit more appreciated. Symmetrical 100Mbps should be possible nowadays.
- Our focus is on uplink, so ADSL type technology will usually be bad
- We prefer one high speed connection, but we can have workarounds for multiple lower speeds. This can be a pain though.
- IP address or addresses we can use to connect, and also that the outside world can connect to. We can work with one address only, but prefer a little more. Three addresses should be plenty. Usually a so called /29 can be provided, that allows for 6 usable addresses.
- The network mask for these addresses
- The default gateway to send our packets to
- The preferred DNS server(s) on this venue, this is optional

Setting up the network at
a new location
# The firewall
First to set up is the firewall. Normally this can be done in at most 30 minutes, since all the inside will remain unchanged. Do this at a convenient desk, not inside the building wiring closet.
Current firewall is a Netgate SG-3100. It has 6 ports at the interesting side, officially the back but use it as front.

Current configuration only uses the rightmost two ports, WAN(The Internet connection), and OPT1(A trunk to the internal network). If the Internet connection is delivered as a fiber(preferably not), it can be converted to standard Ethernet by either using a media converter, or by programming one of the switches(see below) with a special VLAN, one port on fiber, on port on copper.
The SG-3100 firewall is a bit weird in the internal numbering of its network interfaces. They are all called mvnetax for x from 0 to 2. mvneta0 is the OPT1 port, mvneta2 is WAN, and mvneta1(currently unused) is a switch for the LAN1 to LAN4 ports.
To program the firewall, connect a computer to the OPT1 Ethernet interface, check you get an address in the 172.16.0.0/24 network, and connect to https://172.16.0.1.
Username admin, password is wbf123. When doing this in Turkey I had to wait some minutes for the webpages to appear.
For each tournament the internal network should be the same, but the external address or addresses will and VLAN numbers can change. Follow these steps:
1. Set the external IP address. Interfaces→WAN. Change the IPv4 address, do not forget the network mask to the far right in your screen. Click “Add a new gateway”, and fill in the default router address and optionally a description.
2. Now the system has an old and a new gateway. To prevent mistakes throw away the old one. System→Routing. Delete the old, make sure the default IPv4 router is the correct one, and that IPv6 is off.
3. VLAN’s. Interfaces→Assignments→VLANs, Create new VLAN numbers here on the mvneta0 interface for the new setting, do not forget to add a reasonable description for later. This does not change anything yet, but prepares for next step.
   Now go to Interface Assignments. For all networks choose the new assignment of network to VLAN. Do not forget save. This is actual ly the part that changes things.
   To clean things up now go to VLANs again, and delete the old, now unused VLANs.
   The LAN1 to LAN4 ports, although currently unused, are prepared on VLAN 4081-4084 of the mvneta1 interface.
4. Handle external addresses for various services. These have to be set in two places. First goto Firewall→Virtual IPs and change external2 and external 3 to IP addresses other than the WAN address but inside the assigned address range. Now go to Firewall→Aliases and change external1(The real WAN address) and external2 and external3.

This should form a working connection. Now install the firewall at the desired location, and connect the Internet to port WAN. Connect a PC again to port OPT1, which should give an address in the 172.16.0.0 network, but now should also have external access. If all is well disconnect the PC from OPT1, time for bigger things.
If layer1 connect a configured switch to the OPT1 as a trunk. Start building the local network from there. For switch configuration see below.
If layer2 connect the OPT1 port to a switch-port of the building that is configured as trunk.
Automatic backups have been made every night to the Netgate servers, using Services→Auto Configuration Backup.
key: 6e3804d89e60c73e9eba32275d928412b2a8227782905acd25059da8c47ad3ac
encryption password: WbfEbl123
Identifier: wbfebl
At most 100 backups will be stored, so you can restore backups from days ago if needed. It should even be possible to restore backups on different hardware.
# Network management station
A network management station is prepared. It consists of a Lenovo laptop, with docking station and an LG screen. All software runs on this Linux machine. Ip address is 172.16.0.99 and username/password is netman/wbf123.
The switch configuration software is in the directory switchconf. The browser has links for favorites for the rest.
# Switch configuration
We should configure switches as needed. There is software to do that easily. Current configuration, in directory switchconf:
File common:
This file contains site wide definitions. The vlanbase is the lowest number of all our VLAN’s, the vlan definitions map the offset of the vlan to a name. The adminvlan is the vlan where management is done. Aliases can de defined here, for example trunk is a port with network 0 untagged, and 1-9 tagged.
Furthermore there is a list with all types of devices we have, with manufacturer, type and numbers of gigabit and 100Mbit ports.

#
# Allowable VLANs and names
# names will be entered as a synonym for an accessport
# so "vlan 25 foo" will also do "alias foo a25"
#
# For the aliases it is case insensitive
#

vlanbase 30

vlan 0 MGMT
vlan 1 SCORING
vlan 2 EBLWBF
vlan 3 BBO
vlan 4 OTHERVIDEO
vlan 5 GUEST
vlan 6 SECUR
vlan 7 MARIO
vlan 8 SPARE
vlan 9 OLDADMIN

adminvlan 0
network 172.16.0,B:172.16.1

alias trunk u0,t1-9

spanningtree off

#
# All types of hardware supported
# parameters are number of fast(100Mbps) and gig(1000Mbps) ports
#
type cisco sg300-sf 0 10 layer3
type cisco sg300-52 0 52 layer3
type cisco sf300-24 24 4 layer3
type cisco sf302-08 8 2 layer3
type cisco sf302-08mpp 8 2 layer3
type cisco sg200-26 0 26 layer2
type cisco sg200-08 0 8 layer2simple
type fs s1150 0 10 fs

File devices:
This file contains a line for each device, giving the name, the last octet of the IP address, manufacturer, type and the file with the configuration.

#
# All devices with IP adress and HW-type
#

fs10-1 41 fs s1150 istanbul-core
fs10-2 42 fs s1150 istanbul-secondary
fs10-3 43 fs s1150 istanbul-c2-lower
gsw52-1 2 cisco sg300-52 trunk52
gsw26-1 3 cisco sg200-26 scoring26
gsw10-1 4 cisco sg300-sf fibertrunk
sw24-1 11 cisco sf300-24 fotis
sw24-2 12 cisco sf300-24 scoring24
sw24-3 13 cisco sf300-24 scoring24
sw24-4 14 cisco sf300-24 scoring24
sw24-5 15 cisco sf300-24 scoring24
sw8-1 21 cisco sf302-08 scoring10
sw8-2 22 cisco sf302-08 scoring10
sw8-3 23 cisco sf302-08 scoring10
sw8-4 24 cisco sf302-08 scoring10
sw8-5 25 cisco sf302-08 trunk10
sw8-6 26 cisco sf302-08 scoring10
sw8-7 27 cisco sf302-08 scoring10
sw8-8 28 cisco sf302-08 scoring10
sw8-9 29 cisco sf302-08mpp istanbul-sw-c1-corridor
gsw8-1 31 cisco sg200-08 scoring8
gsw8-2 32 cisco sg200-08 scoring8
gsw8-3 33 cisco sg200-08 scoring8
gsw8-4 34 cisco sg200-08 scoring8

Example conf file for a switch
#
# Sample switch
#
port gi1-2 trunk
port fa1-2 mgmt
port fa3 video
port fa4 mario
port fa5-8 eblwbf

## General stuff about switches
These are usually all configured to accept a trunk on the two(10-port version) or four (28-port version) right-most ports, or on port 1 of the 8 port gigabit switches. For fs.com type switches we might at least put the trunks on the SFP ports, we have copper SFP’s for that. Configuration can be done by the webpage (username/password: cisco/wbf123) but for consistency it is recommended to use the makeconf.pl program(or makeconf.exe if you do not have Perl installed), which generates full startup configurations from the .cnf files.

Using the makeconf program configurations can be made by making or editing a configuration file for the switch with the port definitions in the directory conf, if necessary editing the devices file to point to that file. The run the makeconf.pl program; that generates the real configuration files for all switches, and if it has not given any errors the configuration text file for the switch is available if the subdirectory txt..

If we use our own core switch they can be connected to it over fiber if that is convenient in the building. Remember that at the moment we have only four multi-mode SFP’s (Fiber connection points) and no fiber patch cords(well, one test cable). Usually the building has some, but this needs discussion. Fiber patch cords are unfortunately available in many standards. At our side it is the Dual LC/PC connector, but which connector the building patch panels use can vary.
Loading the generated configuration files (.txt) into the Cisco switches:
1. Browse to the switch IP address and login
2. Goto Management/File Management
3. Load configuration file into startup config
4. Reboot the switch

The fs.com switches are similar.
In case the switches become totally messed up the following works: unplug all cables and press the little factory reset button(paperclip needed, in box with core switch!). Keep pressing for about 20 seconds until all lights flash. Switch will reset to factory default, and will listen on address 192.168.1.254, username/password cisco/cisco. Log in (you are forced to change the password), and download a new config.
# Wireless network with Unifi access points

 Since Istanbul 2019 we acquired Unifi access points. These are access points that are programmed by controller software, and run best when this controller is active, but they continue to run without controller.
The controller is installed on the network management station. Access is through a webpage, https://172.16.0.99:8443, login using username/password netman/netman-wbf123
The access points are attached to a trunk network port, but also need power. Either use a POE trunk network port, or use a power injector. There is no possibility to connect a power supply directly to the access points.
The current setup has all existing 5 access points running the same four networks, on both 2G and 5G bands. This can be changed.
SSID	Password	VLAN connected to
bridge-guest	<none>	35
bridge-workers	bridge-workers	32
bridge-bbo	bridge-bbo	33
bridge-scoring-only	kefnrxmhcz	31

If the tournament runs on different VLANs these settings should be changed. Setting ip different SSID’s per group of access points is easy. There is a very good user interface allowing you to look at and change the wireless.
So far the quality of the network is encouraging.

A cloud access method is also possible. I registered the name EblWbfNetman with passwd ebl-wbf-netman. Login at https://unifi.ubnt.com

# Configuring a pfSense firewall (Netgate SG-3100) from scratch

 System / General setup	fill it with sensible data
Interfaces / Assignment	add MGMT on OPT1 interface (mvneta0)
Interfaces / Assignment/VLANs add all the relevant VLANs
add configure interfaces with mask and gateway
disable LAN interface because we don’t use it
disable BBO interface because it is not managed elsewhere
Services / DHCP server	create and enable DHCP servers
Firewall / rules	WAN no extra rule unless required
MGMT allow everything
(assign aliases for more comfort)
(group insecure interfaces to speed up rules creation)
Firewall / NAT	nothing unless needed (port forwarding)
Services / DNS resolver	add needed overrides for relevant names (i.e. unifi)